Car Flagpole Co.

Mounting instruction for car flagpole “Exclusive”.

- Find a suitable vertical position for the car flagpole.            - Use drill guide and mark for 3 drill holes

- Dishes with 10,20,30 and 45 degrees are available,

can be ordered from www.flagpoles.se

- Drill 3 holes – diameter 5,5 mm	   	         - Mount a punch to the middle hole

- Drill the middle hole to 10 mm	  		         - Punch a hole – diameter 25,4 mm (1 inch)

- Paint the edges of the hole

- Mount flagpole holder as picture show

- Mount reinforcing plate inside fender – IMPORTANT	- Mount flagpole with bayonet coupling in

On some car model it could be necessary to adjust 		  mounted holder

plate so its fits fender form.

## Postal address		E-mail			Telephone	        Fax		   Reg.no_______

Angskogsvägen 22b	car@flagpoles.se         +46 705 43 43 97     +46 31 55 18 70	500330-9415

417 43 Goteborg		www.flagpoles.se

Sweden